## Slide 1
KX-NS PBX Remote IP Extension
October 15, 2015
Specifications are subject to change without notice. Program enough TRS (Toll Restriction) level for remote IP extension. “16. Notice for security” in this document is very important.
Panasonic System Networks PBX SE team
Notes: 1

## Slide 2
1. Overview
Built-in MRG feature supports remote IP extension without VPN. Following phones support this feature. - KX-NT543/NT546/NT560 (Version up of phone software is required.) - KX-NT511 and KX-NT550 series - KX-UT / KX-HDV series - 3rd party SIP phone with Blank UDP transmit capability. (Video phone is also supported.) - KX-NT300 based software phone version 4 Other phones do not support this feature. KX-UDT / KX-NT300 (hardware IP phone) series
MRG = Media Relay Gateway
Remote Office or Mobile Internet
192.168.0.1
Local Office
LAN
LAN
WAN 22.33.44.55
192.168.0.101
WAN 11.22.33.44
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
Ext 104
IP address in above picture is example.
Ext 103
KX-NS1000 : Version 3 or later Other KX-NS PBX : Any Version
Notes: 2

## Slide 3
192.168.0.1
Local Office
2. Concept of Programming
LAN
LAN
WAN 22.33.44.55
192.168.0.101 Port : 5060
Only 4 PBX programming are required for remote connection. (1) PBX has to know global IP address of router. 11.22.33.44 (2) PBX has to know SIP port number of router. 15060 (3) Do not forget setting of default gateway. 192.168.0.1 (4) PBX has to know location of each IP extension. Local or Remote Port Fwd is required to router.
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
“5060” is too famous as port for SIP. “5060” has high risk for attacking by hacker. So Port Fwd by router from 15060 to 5060 is required. “15060” is example.
15060 to 192.168.0.101:5060
Ext 103
Remote Office or Mobile Internet
Fixed global IP address is required. DDNS is not supported.
Notes: 3

## Slide 4
Chapter 1 PBX Programming

## Slide 5
11. Assign Global IP Address of Router.
192.168.0.1
Local Office
LAN
192.168.0.101 Port : 5060
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
This document uses “15060” as example. However x50xx such as “15060” and 50xx cannot be programmed from version 4.2 because these are famous as SIP port now. 3xxxx is recommended.
Notes: 5

## Slide 6
12. Assign Default Gateway.
Default gateway is required not only for remote IP extension but also for many other purpose.
192.168.0.1
Local Office
LAN
192.168.0.101 Port : 5060
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Notes: 6

## Slide 7
13. Assign Location of SIP Extension.
< 3rd party SIP Phone >
192.168.0.1
Local Office
Remote Office or Mobile Internet
LAN
LAN
WAN 22.33.44.55
192.168.0.101
WAN 11.22.33.44
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
Ext 103
Notes: 7

## Slide 8
14. Assign Location of KX-NT500.
< KX-NT500 >
Notes: 8

## Slide 9
15. Assign Location of KX-UT.
SBC : Session Boarder Controller (3rd party equipment is required.) Secure communication is available using HTTPs for KX-UT. - TR069(CWMP) is available with https. - Maximum 20 KX-UT phone can use this feature. Each one KX-NS1000 in one-look network supports 20 KX-UT with this feature.
< KX-UT >
Notes: 9

## Slide 10
16. Notice for Security
Program enough TRS (Toll Restriction) level for remote IP extension. International call should be restricted for remote IP extension. Telephone number of international customer of PBX user can be assigned to TRS exception code or system speed dial. Hacker wants to call through some carriers of some countries.
Do not use easy SIP password for remote SIP extension such as “1234abc”. KX-NT/UT is registered by MAC address. However other IP phone including KX-HDV is registered by SIP password.
Notes: 10

## Slide 11
Chapter 2 SIP Phone Setting
SIP Software Phone for Smart-phone by Media5 is used in this chapter as example.

## Slide 12
21. Configure SIP Account.
Notes: 12

## Slide 13
Title = Reference Username = Extension Number Password = SIP Password of PBX
See next page.
22. Assign Ext Number & PIN to log-in.
Notes: 13

## Slide 14
23. Assign Destination to log-in.
192.168.0.1
Local Office
LAN
192.168.0.101 Port : 5060
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Notes: 14

## Slide 15
24. Enable “rport”.
Notes: 15

## Slide 16
Chapter 3 KX-NT/UT Phone Setting

## Slide 17
31. KX-NT500 : Assign Router as Destination.
Assign global IP address of router (11.22.33.44 for example) as destination instead of PBX local address (192.168.0.101 for example), when KX-NT phone is installed in remote office.
192.168.0.1
Local Office
Remote Office or Mobile Internet
LAN
LAN
WAN 22.33.44.55
192.168.0.101
WAN 11.22.33.44
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
Ext 103
Notes: 17

## Slide 18
192.168.0.1
Local Office
Remote Office
LAN
WAN 22.33.44.55
192.168.0.101 Port : 5060
1. Connect KX-UT phone in local office. (Not remote office) 2. Change PBX setting for this extension from “Local” to “Remote”. 3. Restart KX-UT by power off and on again. Error may display but OK. 4. Dispatch KX-UT to remote office. Destination from remote office (11.22.33.44:15060 for example) is automatically informed to KX-UT phone from PBX at step 3.
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
Ext 103
Ext 102 192.168.1.201
32. KX-UT : Connect in Local Office.
11.22.33.44 Port : 15060
Operation is not required in remote office to connect KX-UT phone to PBX. All you have to do is to connect KX-UT phone to LAN in remote office.
Step 4 Dispatch
Notes: 18

## Slide 19
Chapter 4 Router Programming
Port forwarding is required for router.

## Slide 20
Protocol | Range of port number (WAN) | Destination | Description
RTP | 16000-16511(UDP) | 192.168.0.102 | to DSP#1-1
 | 16512-17023(UDP) | 192.168.0.103 | to DSP#1-2
 | 17024-17535(UDP) | 192.168.0.104 | to DSP#2-1
 | 17536-18047(UDP) | 192.168.0.105 | to DSP#2-2
41. Port Fwd to DSP
< for 3rd party SIP Phone / KX-NT500 / KX-UT >
< Reference of PBX setting > Default is OK. This parameter is common for IP trunk and IP extension.
WAN
LAN

## Slide 21
Port number conversion is required from 15060 to 5060.
42. Port Fwd to PBX LAN : SIP
Protocol | Port number | Destination
SIP | 15060(UDP) | 192.168.0.101:5060(UDP)
< for 3rd party SIP Phone >
< Reference of PBX setting > Default is OK.

## Slide 22
Protocol | Port number | Destination
MGCP | 2727(UDP) | 192.168.0.101
PTAP | 9300(UDP) | 192.168.0.101
43. Port Fwd to PBX LAN : KX-NT500
< for KX-NT500 >
< Reference of PBX setting > Default is OK.

## Slide 23
Protocol | Port number | Destination
SIP | 15060(UDP) | 192.168.0.101:5060(UDP)
CWMP (HTTP) | 7547(TCP) | 192.168.0.101
CWMP (HTTPS) | 37547(TCP) | 192.168.0.101
SIP-MLT Data Download (HTTP) | 7580(TCP) | 192.168.0.101
SIP-MLT Data Download (HTTPS) | 37580(TCP) | 192.168.0.101
NTP | 123(UDP) | 192.168.0.101
44. Port Fwd to PBX LAN : KX-UT
< for KX-UT >
< Reference of PBX setting > Default is OK.

## Slide 24
45. Port Fwd to PBX LAN : KX-UT
< Reference of PBX setting > Default is OK. (These should be blank.)
This is applied to above, if above is blank.

## Slide 25
46. Condition for External Router
<Cisco router> Router>enable
Router#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
Router(config)#no ip nat service sip udp port 5060
Router(config)#
Condition for external router is as follows.
- Port Fwd by range setting becomes cause of “No voice” for some router because 16000 (for example) is converted to other number in the range (16000 - 16511). In this case, port fwd for each number is required. 16000 to 192.168.0.102:16000 16001 to 192.168.0.102:16001 : 16511 to 192.168.0.102:16511 - If router has "SIP ALG" feature, this feature should be disabled by programming.
!!! Important !!!

## Slide 26
47. Condition for External Router
- If router does not support port convert such as “15060 to 5060”,
program “15060” as SIP UDP port to PBX.
!!! Important !!!
192.168.0.1
Local Office
LAN
LAN
WAN 22.33.44.55
192.168.0.101 Port : 15060
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
Ext 103
Remote Office or Mobile Internet
15060

## Slide 27
Chapter 5 KX-NS1000 Built-in Router
MRG feature can work with KX-NS1000 built-in router.

## Slide 28
Local Office
51. Concept of Programming
LAN
LAN
WAN 22.33.44.55
192.168.0.101 Port : 5060
Programming (1) and (3) are required for remote connection. (1) PBX has to know global IP address of router. 11.22.33.44 (2) PBX has to know SIP port number of router. 15060 (3 Default gateway programming 192.168.0.101 (No need) (4) PBX has to know location of each IP extension. Local or Remote Fixed global IP address for WAN is required as next page. Other settings such as Port Fwd are NOT required.
WAN 11.22.33.44 Port : 15060
Ext 101 192.168.0.201
Internet
Ext 102 192.168.1.201
Ext 103
Remote Office or Mobile Internet
Activation key KX-NSN101 is required to use WAN.
Notes: 28

## Slide 29
52. IP Address for WAN
Notes: 29

## Slide 30
Thank you !

## Slide 31
Revision
Date | No. | Change
April 17, 2014 | All | First release
June 2, 2014 | 46 | Condition for router was revised.
Nov 5, 2014 | 1 | Software phone version 4 supports MRG.
 | 46 | Condition for router was revised.
April 2, 2015 | 1 (Page 2) | KX-HDV was added.
 | 2 (Page 3) | DDNS is not supported.
 | 2 (Page 3) 11 (Page 5) 51 (Page 28) | This document uses “15060” as example. However x50xx such as “15060” and 50xx cannot be programmed from version 4.2 because these are famous as SIP port now. 3xxxx is recommended.
 | 16 (Page 10) 22 (Page 13) | Notice for security was added.
 | 47 (Page 26) | Condition for router was added.
Oct 15, 2015 | 16 (Page 10) | Notice for security was revised.
Notes: 31